Summary of Series and Parallel Circuits

Series Circuit Characteristics:

    - Voltage:  Kirchhoff’s voltage law:  The total source voltage applied to a series circuit is equal to the total number of individual voltage drops in the series circuit.  VT = sum of all voltage drops.

    - Current:  The current must be the same value at any point in the circuit.

    - Resistance:

RT = R1 + R2 + R3 + …. + RN

The large resistor dominates

    - Power:

PT = VT * IT, and

PT = P1 + P2 + P3 +…….+PN

    - Open circuits across a series resistor cause the current to go to zero everywhere in the circuit.

    - Short circuit across one resistor in a series resistor network causes the current to increase, but the entire circuit is not shorted.

Parallel Circuit Characteristics:

    - Voltage:  The voltage drop across each component is the same as the source voltage.

    - Current:  Kirchhoff’s Current Law:  The sum of the currents into a junction is equal to the sum of the currents leaving that junction.

    - Resistance:

Case 1:  All resistors the same value:  RT = R/N

Case 2:  Two resistors with different values:  RT = R1R2/R1+R2

Case 3:  More than two resistors with different values:

1/RT = 1/R1 + 1/R2 + 1/R3 +…..+1/RN

The small resistor dominates

    - Power:

PT = VT * IT, and

PT = P1 + P2 + P3 +…….+PN

    - Open circuits across a parallel resistor cause no change in the good branches.

    - Short circuit across one resistor in a parallel resistor network causes a dead short across the entire parallel resistor network.