Cornerstone Electronics Technology and Robotics I Week 21

Function Generator and Oscilloscope Lesson 2

- Administration:

  - Prayer

  - Turn in quiz

- Function Generator:

  - A function generator is a device that can produce various patterns of voltage at a variety of frequencies and amplitudes.

  - Our function generator generates sine, triangle & square waveforms from 0.5Hz to 4MHz.

  - The basic controls on a function generator vary the amplitude and frequency of the output waveform.

  - Basic Operation: Perform Oscilloscope/Function Generator Lab 1 – Basic Operation of a Function Generator.

  - Perform Oscilloscope/Function Generator Lab 2 – Offset Function on the Function Generator.

- Electricity and Electronics, Section 10.5, Oscilloscope Continued:

  - Perform Oscilloscope/Function Generator Lab 3 – Displaying a DC Voltage and Dual Display.

  - Perform Oscilloscope/Function Generator Lab 4 – Other Dual Displays.

Electronics Technology and Robotics I Week 21

Oscilloscope/Function Generator Lab 1 – Basic Operation of a Function Generator

- Purpose:  The purpose of this lab is having the student learn the basic controls of a function generator.

- Apparatus and Materials:

  - 1 – Oscilloscope

  - 1 – Function Generator

  - 1 – BNC Male to BNC Male Cable

- Procedure:

  - Select the type of waveform by rotating the Function Switch (FG2).  See the Figure 21 – 1 for the function generator control locations.

  - Select the frequency range by rotating the Frequency Range Selector Switch (FG).

  - Connect the function generator Main Output (FG6) to the CH1 Input Jack (O10) on the oscilloscope.  See the Figures 21 – 2 and 21 - 3 for the oscilloscope control locations.

  - Set the oscilloscope Vertical Mode Control (O13) to CH 1.

  - Adjust the oscilloscope CH 1 Variable Attenuator (O11) to the full clockwise position.

  - Set the oscilloscope CH 1 Volts/Div Control (O12) to 5.

  - Set the oscilloscope CH 1 Input Coupling Switch (O9) to AC.

  - Turn on both the oscilloscope Power Switch (O1) and the function generator Power Switch (FG4).

  - Select different types of waveforms by rotating the function generator Function Switch (FG2).

  - Adjust the amplitude of the waveform by rotating the function generator  Amplitude Control (FG3)

  - Adjust the frequency by changing the function generator Frequency Control (FG5) and Frequency Range Selector Switch (FG1).

  - Set the period of your waveform to 1 ms.  Have the instructor verify.  Calculate the frequency and compare it to the function generator display.

Figure 21 – 1  BK Precision 4003A Function Generator Controls for Lab 1

Figure 21 – 2  BK Precision 2120B Oscilloscope Controls for Lab 1

Figure 21 –  3  BK Precision 2125A Oscilloscope Controls for Lab 1

Electronics Technology and Robotics I Week 21

Oscilloscope Lab 2 – Offset Function on the Function Generator

- Purpose:  The purpose of this lab is to display a dc voltage and a dual voltage trace on an oscilloscope.

- Apparatus and Materials:

  - 1 – Oscilloscope

  - 1 – Function Generator

  - 1 – BNC Male to BNC Male Cable

- Procedure:

  - Set the oscilloscope Vertical Mode Control (O13) to CH 1.

  - Set the oscilloscope CH 1 Volts/Div Control (O12) to 5.

  - Set the oscilloscope CH 1 Input Coupling Switch (O9) to AC.

  - With the function generator, create a sinusoidal waveform with a peak-to-peak voltage of 10 volts.  Ask the instructor to verify your settings.

  - Reset the oscilloscope CH 1 Input Coupling Switch (O9) to DC.

  - Pull the Offset Control on the function generator.

  - Adjust the Offset Control to the – and + sides and observe the waveform on the oscilloscope.  You are adding a dc component to the ac signal.

  - Now adjust the Offset Control until the + peak ac signal is 15 volts. Ask the instructor to verify your settings.

  - Reset the oscilloscope back to CH 1 Input Coupling Switch (O9) to AC.  Notice that the dc component is eliminated.

Electronics Technology and Robotics I Week 21

Oscilloscope Lab 3 – Displaying a DC Voltage and Dual Display

- Purpose:  The purpose of this lab is to display a dc voltage and a dual voltage trace on an oscilloscope.

- Apparatus and Materials:

  - 1 – Oscilloscope

  - 1 – Function Generator

  - 1 – BNC Male to BNC Male Cable

  - 1 – 9 V Battery

- Procedure:

  - Leave the function generator Main Output connected to the CH1 Input Jack on the oscilloscope.

  - Set the Vertical Mode Control to Dual.

  - Connect a scope probe to the CH 2 Input Jack.  The Channel 2 controls are identical to the Channel 1 controls except they are to the right of the Vertical Mode Control.

  - Adjust the CH 2 Variable Attenuator to the full clockwise position.

  - Set the CH 2 Volts/Div Control to 5.

  - Set the CH 2 Input Coupling Switch to DC.

  - Connect the probe’s ground clip to the (–) terminal of the battery.

  - Set the probe slide switch to x1.

  - Connect the probe tip to the (+) terminal of the battery.

  - Turn on both the oscilloscope Power Switch and the function generator Power Switch.

  - Adjust the CH 1 Vertical Position Control and the CH 2 Vertical Position Control such that the ac signal is above the dc signal.

Electronics Technology and Robotics I Week 21

Oscilloscope Lab 4 – Other Dual Displays

- Purpose:  The purpose of this lab is to display circuit inputs and outputs as a dual voltage trace on an oscilloscope.

- Apparatus and Materials:

  - 1 – Oscilloscope

  - 1 – Function Generator

  - 1 – BNC Male to BNC Male Cable

  - 1 – 555 Timer

  - 1 – 74LS04 Hex Inverter

  - 1 – 74LS107 Flip-flop

  - 1 – 74LS47 BCD-to-Seven-Segment Decoder

  - 1 – Jameco 97172 Common Anode 7-Segment Display

  - 1 – 150 Ohm Resistor

  - 2 – 1K Resistors

  - 1 – 10K Resistor

  - 1 – 10K Potentiometer

  - 0.1 Microfarad Capacitor

  - 0.01 Microfarad Capacitor

- Procedure:

  - Inverter Circuit:

    - Wire the 74LS04 inverter circuit below.

Figure 21-4   74LS04 Inverter Circuit

    - Connect the 74LS04 Pin 1 to the CH 1 Input Jack on the oscilloscope and the 74LS04 Pin 2 to the CH 2 Input Jack.

Figure 21 – 5  74LS04 Hex Inverter

Figure 21 – 6   Inverter Truth

    - Observe that the input level (Channel 1) is inverted at the output (Channel 2).

  - Binary Count Circuit:

    - Wire the following dual J-K flip-flop circuit.

    - Use a function generator set at a 1 KHz square wave as the clock input.

    - Connect Q1 to CH 1 Input Jack and Q2 to CH 2 Input Jack on the oscilloscope.

    - Adjust function generator Offset Control to display the Q1 and Q2 output waveforms as shown in Figure 29 – 9 below.

Figure 21 – 7    74LS107 Flip-Flop Pin Layout and Binary Counting Circuit

Figure 21 – 8   Counting to 0 – 3  in Binary

Figure 21 – 9   Q1 and Q2 Outputs

    - Wire the circuit in Figure 21 – 10.

    - Before connecting the binary counting circuit outputs Q1 and Q2 to the circuit, apply the HIGHs (+5V) and LOWs (ground) to pins 7,1,2 and 6 of the 74LS47N as listed in the table below.

    - The 74LS47N is a BCD-to-seven-segment decoder which decodes the Q1 and Q2 signals to illuminate the numbers 0 – 3 on a seven-segment display.  The table lists the input BCD code and the 7-segment display decimal output.

Figure 21 – 10  74LS47 BCD-to-Seven-Segment Decoder Circuit

| BCD Code | 74LS47 Pin Inputs (BCD Code) | 7-Segment |
| --- | --- | --- |
|  | Pin 6 | Pin 2 | Pin 1 (Q2) | Pin 7 (Q1) | Display |
|  | ID | IC | IB | IA | Decimal Output |
| 0000 | 0 | 0 | 0 | 0 | 0 |
| 0001 | 0 | 0 | 0 | 1 | 1 |
| 0010 | 0 | 0 | 1 | 0 | 2 |
| 0011 | 0 | 0 | 1 | 1 | 3 |
| 0100 | 0 | 1 | 0 | 0 | 4 |
| 0101 | 0 | 1 | 0 | 1 | 5 |
| 0110 | 0 | 1 | 1 | 0 | 6 |
| 0111 | 0 | 1 | 1 | 1 | 7 |
| 1000 | 1 | 0 | 0 | 0 | 8 |
| 1001 | 1 | 0 | 0 | 1 | 9 |

    - Now connect Q1and Q2 outputs from the counting circuit above to the decoder circuit.

    - Adjust the function generator frequency (the clock) to about 1.5 Hz.