Cornerstone Electronics Technology and Robotics Week 31

Inductance and RL Circuits

- Administration:

  - Prayer

  - Turn in quiz

  - Oral presentations

- Electricity and Electronics, Section 14.1, Inductance in DC Conditions:

  - Introduction:  The study of electronics revolves around resistance, inductance, capacitance, and the combination of these in series and parallel circuits.  We have already covered resistance in Chapter 3 and capacitance in Chapter 15, now we will study inductance in this chapter.

  - Inductance is the property in electrical circuits that resists a change in current.  Don’t confuse inductance with capacitance which is the property in electrical circuits that resists a change in voltage.

  - An inductor is an electronic component that is used to produce inductance in a circuit.

  - This opposition to a change in current is the result of the energy stored within the magnetic field of the inductor.  Remember that a capacitor opposes a change in voltage by storing its energy in an electric field.

  - Inductance is symbolized by the letter L, measured in henrys (H).  Usually, in electronics smaller values of henrys are used like mH (millihenry).

  - Most inductors have a low dc resistance since they are wound from copper wire.

  - Except for some radio circuits, inductors are not used in modern electronic circuits as often as resistors and capacitors.

  - Other names:

    - Coil

    - Reactor

    - Choke

  - Types:

    - Chokes

    - Tuning Coil

    - Toroidal Coil

  - Symbol:

Inductor			       Transformer

  - Counter emf:

    - When current through an inductor is increased or decreased, the inductor "resists" the change in current by producing a voltage between its leads in opposing polarity to the change.

    - View http://www.williamson-labs.com/480_rlc-l.htm#top

    - This phenomenon exhibits a more general principle known as Lenz's Law, which states that an induced effect will always be opposed to the cause producing it.

From:  http://www.williamson-labs.com/480_rlc-l.htm#top

  - Other References:

    - http://www.allaboutcircuits.com/vol_1/chpt_15/2.html

    - http://www.allaboutcircuits.com/vol_1/chpt_15/1.html

- Slopes:

  - The slope of a line measures the steepness of the line.

  - Slope may be described as “rise” over “run”.

    - Rise means how many units you move up or down from point to point.  On a graph, it would be the change in the y-value.

    - Run on the other hand means how many units you move left or right from point to point.  On a graph, it would be the change in the x-value.

  - Examples of slope:

slope = 0

Graph different slopes, then the values of the slopes on another graph.

Slope Formula:

Slope Formula Given Two Points Given two points and

    - Current/voltage behavior (“Ohm’s Law for an Inductor”):

VL = L x I/t

Where,

VL or EL = Instantaneous voltage across the inductor in volts

L = Inductance in henrys

I/t = Instantaneous rate of current change

The equation relates one variable (in this case, inductor voltage drop, VL) to a rate of change of another variable (in this case, the rate of change of inductor current, I/t).

Circuit conditions for Example 1

Example 1:

Circuit conditions for Example 2

Example 2:

Example 3:

From: http://www.allaboutcircuits.com/vol_1/chpt_15/2.html

  - Resistor/Inductor (R/L) Circuit:

    - L/R Time Constant:

      - Pg 48 pract elect

      - Formula:

L/R

Where:

= Time in seconds for the current to increase to 63.2 % of its maximum value,

L = Inductance in henrys, and

R = Resistance in ohms

- Electricity and Electronics, Section 14.2, Inductance in AC Circuits:

  - Inductance like capacitance is an ac phenomenon.

    - Inductance is frequency sensitive.

    - Signals of different frequencies respond to inductors differently.

  - Inductors ac resistance is called inductive reactance.  Another way of saying it is inductors oppose the flow of ac current; this opposition is called inductive reactance.

    - Formula:

XL = 2fL

Where:

XL = Inductive reactance in ohms,

f = Frequency in hertz, and

L = inductance in henrys

    - Reactance increases with frequency and as the value of the inductance increases.

    - The effect that an inductance has on impeding current flow is analogous to the effect of resistance on impeding current flow in a dc circuit. However, in this case inductive reactance (XL) measured in ohms.

- Applications:

  - LC Low Pass Filter:

    - The circuit below permits lower frequencies to pass through while cutting off higher frequencies.

    - Connect a function generator to the input and an oscilloscope to the output and observe the frequency response of the circuit.

    - Plot the voltage vs. the frequency.

5-Pole Butterworth Low-Pass Filter

From:  Student Manual for The Art of Electronics by Thomas Hayes and Paul Horowitz

  - Bandpass Filter:

    - The following circuit allows a band of frequencies to pass through while suppressing frequencies below and above that band.  The approach to a bandpass filters is to combine a low-pass and a high-pass filter.

    - Connect a function generator to the input and an oscilloscope to the output and observe the frequency response of the circuit.

    - Plot the voltage vs. the frequency.

Wide-Band Bandpass Filter

From Practical Electronics for Inventors by Paul Scherz