Electronics Review 1

Cornerstone Electronics Technology and Robotics II Week 1

- Administration:

  - Prayer

  - Welcome back

  - Review Quiz 1

- Review:

  - Reading meters:

    - When a current or voltage value is unknown, begin with the highest meter range.

    - An ammeter must always be connected in series (in line) with a circuit component.

    - Voltmeters are always connected in parallel with the component (across the component).

    - When measuring resistance, disconnect the resistor from the circuit.  Also make sure power is off to the circuit.

  - Ohm’s Law:

V = I x R where:

V = voltage in volts,

I  = current in amperes, and

R = resistance in ohms

  - Switches:

    - SPST switch example and symbol:

    - SPDT switch example and symbol:

    - DPDT switch example and symbol:

    - Momentary switches:

Normally Closed (NC)	    Normally Open (NO)

    - Show samples

  - Potentiometer: a 3 -Terminal Variable Resistor

    - 100 Watt sample

    - Potentiometer Symbol:

    - Function:

Potentiometer

      - The resistance between points A and C (RAC) is constant.  It is the resistance rating of the potentiometer.

      - As wiper B moves up and down the potentiometer, resistances RAB and RBC vary, but RAB + RBC will equal RAC.

      - Set up an experiment to verify the last point.

  - Rheostat:  A 2 -Terminal Variable Resistor

    - Symbol:

Rheostat

    - Potentiometer Wired as a Rheostat:

Circuit A	    Circuit B		 Circuit C

      - In the Circuits A and B above, a potentiometer is used as a rheostat.

      - In Circuit A above, RAB is always 0 Ohms and RBC varies from 0 – 100K Ohms.

      - In Circuit B, RBC is always 0 Ohms and RAB varies from 0 – 100K Ohms.

      - In Circuit C, RAB varies from 0 – 100K Ohms and RBC does not exist since there is no connection to C.

      - What is the purpose of the 470 ohm resistor?

  - Review Summary Sheet of Series and Parallel Circuits

    - See:  http://www.cornerstonerobotics.org/curriculum/lessons_year1/ER%20Week13a,%20Series%20Parallel%20Summary.pdf

  - Parallel Resistors:

    - Perform Review 1 Lab 1 – Voltage Drop in a Parallel Circuit

  - Voltage Dividers:

    - Series resistors can be used to divide a voltage into smaller voltages.  For example, the following series resistors divide a 12 volt source into 12 volts, 8 volts, and 4 volts using the same value for each resistor.  Notice that we are not measuring voltages across each resistor, but voltages from a point, e.g. B to the ground point D (VBD).  (The voltage drop across each individual resistor is 4 volts.)

Example of a Voltage Divider

    - Potentiometers can be used as voltage dividers.  In the circuit below, the sum of the voltmeter measurements VAB and VBC equals the source voltage VAC.

Potentiometer as a Voltage Divider

    - Voltage dividers may be used in resistive sensor circuits

    - Perform Review 1 Lab 2 – Potentiometers.

  - Kirchhoff’s Current Law:  The sum of the currents into a junction is equal to the sum of the currents leaving that junction.

    - Parallel circuits act as current dividers.

Example 1					     Example 2

- 14” Band Saw:

  - Safety Rules:

    - See copy from the manual.

  - Operation:

    - See copy from the manual.

- Project for the Year:

  - Each student will design and build his own mobile autonomous robotics car.  The car must be equipped to:

    - Use dc motors as the drive system

    - Have sufficient room on a breadboard for a LCD (Liquid Crystal Display), PIC microcontroller(s), H-bridge, and other supporting electronics

    - Mount several different sensors that will be studied this year

- Practice Circuit:

  - Perform Review 1 Lab 3 – Touch Switch.

Cornerstone Electronics Technology and Robotics II Week 1

Electronics Review 1 Lab 1 – Voltage Drop in a Parallel Circuit

- Purpose:  The purpose of this lab is to experimentally verify that the voltage drops across parallel resistors are equal.

- Apparatus and Materials:

  - 1 – Solderless Breadboard with 9 V Power Supply

  - 1 – Digital Multimeter

  - 1 – 1 K Ohm Resistor

  - 2 – 2.2 K Ohm Resistors

  - 1 – 4.7 K Ohm Resistor

- Procedure:

  - Wire the following circuit

  - Measure and record VAE, VBF, VCG, and VDH.

- Results:

- Conclusions:

  - How do the voltage drops VAE, VBF, VCG, and VDH mathematically relate to each other?

Cornerstone Electronics Technology and Robotics II Week 1

Electronics Review 1 Lab 2 – Potentiometers

- Purpose:  The purpose of this lab is have the student measure tripot values and to help the student understand the function of a potentiometer as a variable resistor.

- Apparatus and Materials:

  - 1 – Digital Multimeter

  - 1 – 5 K Ohm Potentiometer

- Procedure:

  - Testing potentiometers:

    - Test and record the maximum resistance of the potentiometer with a DMM, and compare with value printed on the side of the potentiometer.

    - Turn the potentiometer shaft and then flip the DMM leads.  How does the maximum resistance value of the potentiometer react?  Record your results.

    - Using the DMM, measure and record the resistance RAB, RBC, and RAC at three different positions of the potentiometer.  Before changing each position, apply +5v to Point A and ground to Point C, then measure and record VAB, VBC, and VAC.

- Results:

  - Maximum resistance of the potentiometer:

Maximum resistance = _______________ohms

Printed value of the potentiometer = ______________ ohms

Resistance when potentiometer shaft turned = _________ohms

Resistance when DMM leads reversed = _____________ohms

  - Testing potentiometers:

- Conclusions:

  - In the potentiometer test, mathematically relate RAC to RAB and RBC.

  - How does VAC relate to VAB + VBC?

Cornerstone Electronics Technology and Robotics II Week 1

Electronics Review 1 Lab 3 – Touch Switch

- Purpose:  The purpose of this lab is to reacquaint the student with wiring a circuit on a breadboard.

- Apparatus and Materials:

  - 1 – 555 Timer

  - 1 – 10M Resistor

  - 1 – 100K Resistor

  - 1 – 1K Resistor

  - 1 – 0.01 uF Capacitor

  - 1 – 4.7uF, 10uF, 22uF, 47uF, and 100uF Capacitors

  - 1 – LED

- Procedure:

  - Wire the touch switch circuit on your breadboard.

  - Use a 4.7 uF capacitor for C2 to begin, and then substitute the 10 uF, 22 uF, 47 uF, and 100 uF in its place.

  - Use the normal jumpers as your touch leads.